## Slide 1
PROJECT PRESENTATION • 2025–26
Industrial Carbon Credits
Calculator
A UNFCCC CDM-compliant web tool for emission accounting, carbon credit estimation and India CCTS 2025 compliance reporting
Net CERs = Baseline Emissions − Project Emissions − Leakage
Presented by: [Your Name] | Guide: [Faculty Name]
Department of [Department] • [Institution] • May 2026

## Slide 2
OUTLINE
Table of Contents
01
Introduction & Motivation
Why industrial carbon accounting matters
02
Literature Review
Global standards & Indian regulatory framework
03
Model Prepared — The Tool
Architecture, formula and 11-industry coverage
04
Methodology — 6-Step Workflow
From industry selection to results dashboard
05
Project Emissions Engine
Eight tabs across Scope 1, 2 and 3
06
Case Study — Ultratech Cement
Aditya Cement Works, Chittorgarh
07
Conclusions & Future Scope
Findings, limitations and next steps
08
References
Standards, datasets and reports cited
Industrial Carbon Credits Calculator • UNFCCC CDM Standard
2

## Slide 3
01 • INTRODUCTION
Why a Carbon Credits Calculator?
Industrial sectors — cement, steel, power, refineries — contribute the largest share of global CO₂ emissions. Under India's Carbon Credit Trading Scheme (CCTS 2025), every covered facility must now report its Greenhouse-Gas Emission Intensity (GEI) and either earn or purchase carbon credits to stay compliant.
THE PROBLEM
Most plant managers lack a single, standards-based tool that translates fuel bills, electricity meters and process data into credit-grade tCO₂e numbers.
Spreadsheets fragment the workflow, miss the latest IPCC AR6 / India CEA factors, and cannot generate audit-ready reports.
30%
of global CO₂ emissions come from heavy industry
11
industrial sectors covered by the tool
8
emission categories tracked across Scope 1 / 2 / 3
6
guided steps from sign-in to PDF report
Industrial Carbon Credits Calculator • UNFCCC CDM Standard
3

## Slide 4
02 • LITERATURE REVIEW
Standards & Frameworks Studied
Before development, the team reviewed the international and Indian frameworks governing industrial carbon accounting. The calculator embeds emission factors and rules drawn from the seven sources below.
INT'L
UNFCCC CDM
United Nations Clean Development Mechanism — the canonical 'BE − PE − Leakage' formula adopted by the tool.
SCIENCE
IPCC AR6 & 2006 Guidelines
Source for default calorific values, emission factors and GWP100 (e.g. CH₄ = 27).
GRID
India CEA UCR CoU 2025
National grid emission factor (0.736 kgCO₂/kWh) used for Scope 2 electricity.
PRIVATE
Verra VCS
Verified Carbon Standard — voluntary-market certification compatibility.
SECTOR
GCCA / World Steel Association
Sector benchmarks: e.g. OPC Portland cement = 0.92 tCO₂/t (GCCA COP29 2024).
INDIA
BEE CCTS Notification 2025
Govt GEI upper-ceiling values for compliance under the Carbon Credit Trading Scheme.
INDIA
MoEFCC GEI Target Rules 2025
Sub-sector baseline intensities (FY 2023-24) and pro-rata FY 2026-27 targets.
PROTOCOL
GHG Protocol
Scope 1 / 2 / 3 classification used to organise the eight emissions tabs.
Industrial Carbon Credits Calculator • UNFCCC CDM Standard
4

## Slide 5
03 • MODEL PREPARED
The Tool at a Glance
CORE FORMULA (UNFCCC CDM)
Net CERs = BEy − PEy − LEy
DEPLOYMENT
Web-based
Built on Lovable; runs in any browser (Chrome / Edge / Firefox). Google Sign-In persists analyses across devices.
INDUSTRIES
Coverage
11 industries: Cement, Steel, HCl, Soda Ash, Fertilizer, Paper & Pulp, Refinery, Textiles, Power, Aluminum, Other.
DELIVERABLES
Outputs
Interactive dashboard, waterfall + pie charts, plus two PDF reports — Concise Summary and Detailed GEI Report.
LIVE TOOL › https://eco-carbon-path.lovable.app
Industrial Carbon Credits Calculator • UNFCCC CDM Standard
5

## Slide 6
04 • METHODOLOGY
Six-Step Guided Workflow
1
Industry
Pick from 11 sectors
2
Company
Plant, year, region, grid EF
3
Baseline
Benchmark / historical / regulatory
4
Project
8 tabs: fuel → Govt GEI
5
Leakage
Default 5% or certified value
6
Results
Dashboard + PDF report
WHAT EACH STEP CONTRIBUTES
Steps 1–2 scope the facility and load the right region/sector emission factors automatically.
Step 3 fixes the 'business-as-usual' reference (BE) — without this, no credit can be claimed.
Step 4 captures actual emissions (PE) across all three GHG-Protocol scopes, plus reductions and Govt-GEI compliance.
Steps 5–6 deduct leakage and present the final Net CERs along with downloadable, audit-ready PDF reports.
Industrial Carbon Credits Calculator • UNFCCC CDM Standard
6

## Slide 7
05 • EMISSIONS ENGINE
Eight Tabs Across Scope 1, 2 and 3
SCOPE 1
Direct
What the plant burns or releases on-site
Fuel Combustion
Coal, petcoke, NG, diesel — IPCC CV & EF auto-filled
Process Emissions
e.g. limestone calcination CaCO₃ → CaO + CO₂
Fugitive Gases
CH₄ leaks, HFCs, purge gas — GWP from IPCC AR6
SCOPE 2
Energy
Purchased grid electricity
Electricity
kWh × Grid EF (0.736 kgCO₂/kWh — India CEA 2025)
SCOPE 3
Indirect
Up- and down-stream value chain
Transport
Truck = 0.062, Ship = 0.011 kgCO₂/t-km
Waste
Landfill / treatment / incineration / recycling
+ Reductions tab (renewables, CCUS, biomass, energy-efficiency, waste-heat recovery) + Govt GEI tab (India CCTS 2025 compliance check against MoEFCC / BEE limits)
Industrial Carbon Credits Calculator • UNFCCC CDM Standard
7

## Slide 8
06 • CASE STUDY
Ultratech Cement — Aditya Cement Works
Plant: ADITYA CEMENT WORKS, Chittorgarh | Sub-Sector: Cement — Clinkerization | FY 2025-26 | Production: 10,000 t/yr
Project Emissions by Source (tCO₂e)
Chart: 
| Process (57%) | Fuel (26%) | Electricity (7%) | Transport (6%) | Waste (3%) | Fugitive (<1%)
Emissions | 5838 | 2651 | 736 | 625 | 324 | 27
9,200
Baseline (BE)
tCO₂e
9,701
Project (PE)
tCO₂e
0
Net CERs
tCO₂e
1,671
Credits to buy
tCO₂e
GOVT GEI COMPLIANCE • INDIA CCTS 2025
✕ NON-COMPLIANT
Baseline GEI: 0.82 tCO₂e/t Govt Limit: 0.803 Actual: 0.97 tCO₂e/t
Credits to purchase = (0.97 − 0.803) × 10,000 = 1,671 tCO₂e
KEY INSIGHT
Calcination alone drives 57% of total emissions, confirming the IPCC observation that process CO₂ — not fuel — is the dominant lever in cement decarbonisation. Reducing the clinker factor would have the largest single impact on this plant's GEI score.
Industrial Carbon Credits Calculator • UNFCCC CDM Standard
8

## Slide 9
07 • CONCLUSIONS
Findings, Limitations & Next Steps
01
Standards-grade
The tool faithfully implements the UNFCCC CDM formula with IPCC AR6 / India CEA 2025 default factors — no spreadsheet reinvention needed.
02
Compliance-ready
Auto-checks emissions against MoEFCC GEI baselines and BEE CCTS upper-ceilings, flagging credits to buy or earn in real time.
03
Decision-useful
Waterfall and pie visualisations point straight to the dominant emission lever (e.g. calcination = 57% in cement).
LIMITATIONS
Default emission factors are not a substitute for facility-specific lab-tested values during formal audits.
Leakage uses a flat 5% industry default unless a certified value is supplied.
Output is for planning; formal CCTS submission must still be cross-verified on the BEE portal.
FUTURE SCOPE
Direct API hook into BEE portal for one-click compliance filing.
Multi-plant rollup with year-on-year trend dashboards.
Marginal-abatement cost curve so users see the cheapest CO₂ reduction first.
Verra VCS / Gold Standard report templates for voluntary-market projects.
Industrial Carbon Credits Calculator • UNFCCC CDM Standard
9

## Slide 10
08 • REFERENCES
Standards, Datasets & Reports Cited
YEAR
ORG / SOURCE
REFERENCE
2006
IPCC
2006 IPCC Guidelines for National Greenhouse Gas Inventories. Vols. 2 (Energy) & 3 (Industrial Processes & Product Use).
2021
IPCC
Sixth Assessment Report (AR6), Working Group I — Global Warming Potential values used in the Fugitive-Gases tab.
2024
IEA
International Energy Agency — World energy balances and sectoral emission factors.
2025
CEA
Central Electricity Authority of India — User Compliance Report (UCR) CoU 2025: India National Average Grid EF = 0.736 kgCO₂/kWh.
2025
MoEFCC
GEI Target Rules 2025 — Sub-sector baseline emission intensities (FY 2023-24) and pro-rata FY 2026-27 targets.
2025
BEE
Bureau of Energy Efficiency — Carbon Credit Trading Scheme (CCTS) Notification 2025: sectoral GEI upper ceilings.
2024
GCCA
Global Cement & Concrete Association, COP29 benchmark: OPC Portland = 0.92 tCO₂/t cement.
—
WSA
World Steel Association — sectoral CO₂ intensity benchmarks for steel production routes.
—
WRI/WBCSD
Greenhouse Gas Protocol — Corporate Accounting & Reporting Standard (Scope 1 / 2 / 3 framework).
—
UNFCCC
Clean Development Mechanism (CDM) Methodologies — source of the Net CERs = BE − PE − LE formula.
THANK YOU • QUESTIONS? Tool: https://eco-carbon-path.lovable.app
Industrial Carbon Credits Calculator • UNFCCC CDM Standard
10